## Slide 1
EMD 531
Lecture 3
Chantal Vogels, PhD
The pathogen sequencing toolbox

## Slide 2: Learning objectives
Students will be able to
Explain next-generation sequencing
Compare different sequencing approaches and platforms
Choose appropriate sequencing methods to answer questions

## Slide 3: Pathogen genomics workflow
Armstrong et al. (2019) NEJM

## Slide 4: What is next-generation sequencing?

## Slide 6
 | Sanger | Next-generation sequencing
Sample size | 1 strand per base | 1 strand per sequence
Speed | Single reads | Massively parallel
Cost (human genome) | $10.000.000 | $1.000
Accuracy | Low | High (higher coverage)
Read length | Long (700-1000bp) | Short (100-200bp)
EMBL-EBI: NGS Practical Course

## Slide 7: Sequencing approaches and platforms

## Slide 8
Pathogen RNA or DNA
Host RNA
Host DNA
Total Nucleic Acid

## Slide 9
Illumina
Nanopore
Ion
Pacbio
BGI

## Slide 10: Challenges in sequencing of pathogens
Viruses
E.g. Zika virus: 11kb
 Whole genome
Bacteria
E.g. Mycobacterium tuberculosis: 4.4Mb
 16S rRNA
Protozoa
E.g. Plasmodium falciparum: 22.9Mb
 Targeted genes
Kooij et al. (2005) PLOS Pathogens
Cole et al. (1998) Nature
Viral Zone

## Slide 11: Whole genome versus targeted gene sequencing
Dudas & Bedford (2019) BMC Evolutionary Biology

## Slide 12: How to match a method with a question?

## Slide 13
Question + Samples + Resources = Tool

## Slide 14: Question
What pathogen is in my sample?
  Unknown – need unbiased method
  Sequencing depth – need lots of data/sample
How is the pathogen evolving during an outbreak?
  Known – can use a targeted method
  Sample size – need to sequence lots of viruses
How is the pathogen evolving within a host?
  Known – can use a targeted method if accurate
  Sequencing depth – need lots of data/sample

## Slide 15: Samples
Target to background ratio
  Sample type and pathogen dependent (e.g. Zika virus in serum)
    CT values, house-keeping genes, total nucleic acid, carrier RNA?
  Determines unbiased versus targeted approach
Integrity
  RNA/DNA extraction and storage
  Determines read/amplicon lengths

## Slide 16: Resources
Money $$
  Do you have enough $$ to generate the required data?
  Determines library prep and platform
Time
  How quickly do you need the data?
  Determines platform
Environment
  Fully-equiped molecular biology lab? With personal sequencer?
  Access to a genomics core?
  In the field or other resource-limited environment?
  What capacity do you have to analyze data?
  Determines library prep and platform
Don’t be an ”Illumina Lab” just because you have a MiSeq

## Slide 17
Question + Samples + Resources = Tool
Tool = Library prep + Sequencing platform

## Slide 18: Tools – Library prep
Untargeted metagenomics
  Sequence everything
  Slightly biased additions
    Dnase treatment
    Host RNA depletion (e.g. rRNA)
Pros
  Gold standard for pathogen sequencing (limited biases)
  Do not need to know what you are looking for
Cons
  Often requires lots of data/sample to cover target
  Computationally challenging

## Slide 19: Tools – Library prep
Targeted/enriched metagenomics
  Sequence mostly target, but other stuff too
  Examples
    Spiked-primers during cDNA synthesis
    Target capture probes pre or post library prep
Pros
  Enhance target sequencing with minimal biases
  Can scale for lots of potential targets (all DENV, all flaviviruses, all viruses)
Cons
  Increases time, money, and skill of library prep

## Slide 20: Tools – Library prep
Targeted PCR amplification
  Sequence only target
  Examples
    16S for bacteria
    Overlapping multiplexed for near-complete virus genomes (PrimalSeq)
Pros
  Cheap and easy
  Scalable for generating large datasets
  Requires minimal sequencing data
Cons
  Biased amplification
  Easy to contaminate

## Slide 21: Tools – Library prep
Culture isolation and selection
  Isolate bacteria from growth medium
  Enrich for virus in cells prior to standard sequencing
  Grow protozoa in culture
  Still commonly used in surveillance programs
Pros
  Broad enrichment for pathogens that easily replicate in culture
  Mostly pathogen RNA/DNA, requires minimal sequencing data
  Cheap
Cons
  Biased pathogen composition (among species and intra-host populations)
  Potential for culture selection and adaptations

## Slide 22: Tools – Sequencing platform
Large-Scale
  E.g., Illumina NovaSeq, HiSeq; PacBio; Nanopore PromethION
  Most data/$, but expensive per run
  Not affordable by most individual labs (genomics cores)
Mid-Scale
  E.g., Illumina MiSeq, NextSeq; Ion Torrent; Nanopore GridION
  mid data/$
  Affordable by some individual labs, requires maintenance
Portable
  E.g., Illumina iSeq; BGI DNBseq; Nanopore MinION
  Low data/$, but cheap per run
  Affordable and can be set up in many locations

## Slide 23: Tools – Sequencing platform
Maccannell. 2018. Platforms and Analytical Tools Used in Nucleic Acid Sequence-Based Microbial Genotyping Procedures

## Slide 24: Tools – Sequencing platform
Platform | Expected Yield (Gb) | Seq Kit Cost | Estimated Cost/Gb
Illumina iSeq | 1 | $600 | $600.00
Illumina MiSeq | 15 | $1,625 | $108.33
Illumina HiSeq | 1500 | $6,810 | $4.54
Illumina NovaSeq | 6000 | $5,500 | $0.92
ONT MinION | 10 | $675 | $67.50
ONT GridION | 150 | $3375 | $22.50
ONT PromethION | 3800 | $19,200 | $5.05

## Slide 25: Tools – Sequencing platform
  Accurate sequencing, short reads
  Good for generating lots of data (NovaSeq)
  Expensive to run and maintain
  Uses:
    Large projects (samples in home lab)
    Accurate sequencing (intrahost, metagenomics)
Illumina
  Long reads, error prone
  Good for generating quick data
  Rugged, cheap to run (reusable flowcells)
  Uses:
    Field or limited resources
    Lab for long reads and quick data
MiSeq/NovaSeq

## Slide 26: Controls + accuracy
Controls
  Negative controls at important steps (sample collection, RNA extraction, PCR, etc)
  “Healthy” or environmental controls (metagenomics to determine background)
  Internal controls to measure efficiency of library prep and validate sequencing
  Normalize input target concentrations (important for comparing intrahost diversity)
Improving accuracy
  Dual-indexes (reduces “index” hopping)
  High-fidelity polymerases (reduces library prep errors)
  Sequence technical replicates (removes sequencing errors)
  Unique molecular identifiers (UMIs, removes sequencing errors)

## Slide 27: Class activity: Sequencing approaches for mock scenarios

## Slide 28
Library prep
Platform
Illumina
Nanopore
MiSeq
NovaSeq
MinION
Untargeted
Targeted
Metagenomics
Amplicon
PollEv.com/cvogels425

## Slide 29: Scenario #1
Question
  An unknown pathogen causing an outbreak of pneumonia in Wuhan, China
Samples
  Blood and sputum samples
  Dozens of samples
Resources
  State-of-the-art molecular lab
  No genomics core
  Need data fast
Tools?
Library prep
Platform
PollEv.com/cvogels425

## Slide 30: Scenario #2
Question
  Clinical metagenomics for unknown causes of encephalitis (population study, not for diagnostics)
Samples
  Cerebral spinal fluid, maintained on cold chain
  Hundreds of samples
Resources
  Well funded clinical lab
  Access to Genomics Core
  Not time sensitive
Tools?
Library prep
Platform
PollEv.com/cvogels425

## Slide 31: Scenario #3
Question
  Investigating 2019 dengue virus outbreak in Honduras
Samples
  Serum, low CTs, somewhat degraded
  Hundreds of samples
Resources
  Mobile field lab
  Need data fast
Tools?
Library prep
Platform
PollEv.com/cvogels425

## Slide 32: Scenario #4
Question
  Characterizing drug-resistance genes in Mycobacterium tuberculosis
Samples
  Sputum samples
  Dozens of samples
Resources
  Basic molecular lab
  Time sensitive
Tools?
Library prep
Platform
PollEv.com/cvogels425

## Slide 33: Scenario #5
Question
  Identifying SNPs in Plasmodium falciparum virulence genes
Samples
  Serum samples
  Dozens of samples
Resources
  Well funded clinical lab (not much NGS experience)
  Access to Genomics Core
  Not time sensitive
Tools?
Library prep
Platform
PollEv.com/cvogels425

## Slide 34: Scenario #6
Question
  Are two mutations ~500nt apart co-occurring on the same virus genome (pilot study)?
Samples
  Cell culture supernatant, mixed infections
  Few samples
Resources
  Basic molecular lab
  Need data fast for PhD committee meeting
Tools?
Library prep
Platform
PollEv.com/cvogels425

## Slide 35: Scenario #7
Question
  Determining possible co-infections (bacteria and viruses) in ticks
Samples
  Ticks
  Hundreds of samples
Resources
  State-of-the-art molecular lab
  Access to Genomics Core
  Not time sensitive
Tools?
Library prep
Platform
PollEv.com/cvogels425

## Slide 36: Scenario #8: Your scenario?
Tools?
Library prep
Platform
PollEv.com/cvogels425

## Slide 37
  github.com/grubaughlab/path-gen_resources